## Slide 1: Smart Robotics - System Design
Diego Alfredo Cerda Torres
A01281978
Claudia Xochitl Pérez Ortiz
A01196602

## Slide 2
Processing system
Actuator system
Sensing system
CAN
J1939
(communication layer)
Mensajes CAN de
velocidad
Mensajes CAN de
desplazamiento
Posición con PGN específico
Desplazamiento con PGN específico
Microcontroller STM32
Communication protocol
Data
Data
Eelctric supply
Fluctuating power
demand
Fluctuating power
demand
Fluctuating power
supply
other systems
Fluctuating power
demand
Environment
Temperature
Humidity
Error codes (DTC, FMI)
Context diagram

## Slide 3: Functional hierarchical diagram
Smart processing
Read sensor messages
Interpret speed message
Send actuator messages
Send position
Send orientation
Codify information in specific PGN
Decodify identifier bits
Read Data bits
Find PGN in documentation, priority, and source address
Search SPN for speed
Find PGN for position
Set data bits in specific SPN position
Send frame
Find PGN for position
Set data bits in specific SPN position
Send frame
Codify information in PGN
Manage errors
Read potential error
Read DTC field
Find FMI bits
Find cause associated
Ignore message in calculations
Calculate position and orientation
Get kinematic model of velocity
Transform in into generalized coordinated vector (with x, y, theta)
Separate angular and linear velocity
Calculate linear and angular displacement
Calculate displacement and orientation from starting pose

## Slide 4: Requirements
Functional The subsystem shall communicate the sensor and the actuator. The subsystem shall interpret the CAN data (velocities) frame from the sensor subsystem. The subsystem shall send position and orientation information (as a CAN data frame with a specific PGN) to the actuator subsystem. The subsystem shall manage errors in the system. The subsystem shall calculate the orientation and position of the system | Performance The subsystem shall set the starting pose (x, y, theta). The subsystem shall set the time step. The subsystem shall get the kinematic model of the velocity. The subsystem shall transform the model into a generalized vector. The subsystem shall calculate angular and linear velocity. The subsystem shall calculate relative position and orientation. The subsystem shall detect errors and ignore them in calculations.
Design Constraints The subsystem shall utilize CAN module. The subsystem shall use J1939 standard. The subsystem shall be programmed through Matlab. The subsystem shall be programmed in Model Based Software Development (MBSD). The subsystem shall be programmed into a STM32 (STM32f103c8t6). | Quality attributes The subsystem shall send the information in less than 0.5 seconds. The subsystem shall have a position precision of *the defined by the higher authority* The subsystem shall have an orientation precision of *the defined by the higher authority* The subsystem’s processor shall operate in temperature between -40 and +85 °C. The subsystem’s processor shall operate with a voltage ranging from 2.0 to 3.6 V. The subsystem shall opérate with a Vin between 3.3 and 5 V.